## Slide 1
MOTOR
MOTOR
ESC
ESC
BMS
ANTI-SPARK SWITCH
CHARGER
DC/DC
NEBENVERBRAUCHER
BATTERIE
BATTERY
DC/DC
ON/OFF SWITCH
5V Sub-System
36V Sub-System

## Slide 2
BATTERY CELL 3,7V
BATTERY CELL 3,7V
BATTERY CELL 3,7V
BATTERY CELL 3,7V
BATTERY CELL 3,7V
BATTERY CELL 3,7V
BATTERY CELL 3,7V
BATTERY CELL 3,7V
BATTERY CELL 3,7V
BATTERY CELL 3,7V
BATTERY CELL 3,7V
BATTERY CELL 3,7V
BATTERY CELL 3,7V
BATTERY CELL 3,7V
BATTERY CELL 3,7V
BATTERY CELL 3,7V
BATTERY CELL 3,7V
BATTERY CELL 3,7V
BATTERY CELL 3,7V
BATTERY CELL 3,7V
BMS
B-
P-/C-
P- / C-
B+
discharging / charging positive
discharging / charging negative

## Slide 3
BMS
CHARGER
BATTERIE
BATTERY
INPUT: 100V-240V AC OUTPUT: 42 V DC – 2.0 A
36 V – 10 S – 35 A
INR18650-25R Rapid charge CC-CV, 4A, 4.20 ± 0.05 V, 100mA cut-off Discharge cut-off voltage/ End of discharge 2.5V
Overcharge Detection Voltage | 4.28 ± 0.05 V
Overcharge Protection Delay | 100 mS
Overcharge Cancel Voltage | 4.08 ± 0.05 V
Balance Detection Voltage | 4.2 ± 0.025 V
Balance Cancel Voltage | 4.2 ± 0.05 V
Balance Current | 56 ± 5 mA
Over-discharge Detection Voltage | 2.55 ± 0.08 V
Over-discharge Detection Delay | 50 mS
Over-discharge Cancel Voltage | 3.0 ± 0.1 V
Overcurrent Detection Voltage | 150 mV
Overcurrent Detection Delay | 15 mS
Overcurrent Protection Current | 120 ± 5 A
Protection Cancel Condition | Disconnect Load
Short Circuit Protection Condition | Outside Load Short Circuit
Short Circuit Detection Delay | 200 uS
Protection Cancel Condition | Disconnect Load
 | -30℃ ~ +80℃
Continuous Discharge Current | 35 A
Momentary Discharge Current | 100 A